## Slide 1: Evaluating the Impact of Interconnections in Quantum-dot Cellular Automata (QCA)
Frank Sill Torres1,2, Robert Wille1,3, Marcel Walter2, Philipp Niemann1,2, Daniel Große1,2, Rolf Drechsler1,2
1DFKI GmbH (Germany), 2University of Bremen (Germany)
3JKU Linz (Austria)

## Slide 2: Outline
Motivation
Design Automation
Analysis Environment
Results
Conclusions

## Slide 3: Motivation
Quantum-dot Cellular Automata (QCA)
Promising nanotechnology based on quantum dots
Remarkable low energy dissipation
Several (experimental) physical realizations based on different concepts (Metal islands, nanomagnets, dangling bonds, …)
Metal islands
Nanomagnets
Dangling bonds

## Slide 4: Motivation
Challenging routing in QCA
  QCA is (nearly) planar technology
    Current state: 1 layer for logic & routing, 1 layer for crossings
    Outlook: low amount of layers
  Data flow must follow clocking constraint (clock 1 → clock 2 → clock 3 → … )
  Only orthogonal routing
Simple example:
Interconnections
Routing overhead

## Slide 5: Motivation
More complex design
Interconnections with notable impact on Area, Delay, Energy increase
Question: What is the actual impact?
Interconnections cont’d

## Slide 6: Design Automation
Comparison
CMOS Process
QCA Process
Transistors and
connections
MOS layers
QCA cells and
its positions
Layers of specific material
No Differences
Some Differences

## Slide 7: Design Automation
Principal Flow
HDL Description
Netlist
Tile (clock zone) grid
Layout

## Slide 8: Design Automation
Gate Library
Routing Elements
Simple Gates
Complex Gates
Wire
Bent wire
Fanout
Inverter
Majority
OR
NOR
XOR

## Slide 9: Design Automation
Components of energy dissipation of QCA:
Dissipated energy: Eenv = Eclk + Ein – Eout
QCADesigner-E - Physics simulator including determination of energy dissipation of QCA (https://github.com/FSillT/QCADesigner-E)
Energy Model
-
-
Eclk - Energy from clock
Eenv - Energy to environment
Eout - Energy to neighboring cell(s)
Ein - Energy from neighboring cell(s)

## Slide 10: Design Automation
Characterized Gate library
 |  | Area [µm²] | Delay [tiles] | Energy Disspation [meV] |  |  |  |  | 
 |  |  |  | Regl. Mode (25 GHz) |  |  | Fast mode (100 GHz) |  | 
 |  |  |  | 000 | ... | 111 | 000 | ... | 111
Routing Elements | Wire | 0.01 | 1 | 0.09 | ... | - | 0.82 | ... | -
 | Bent-wire | 0.01 | 1 | 0.10 | ... | - | 0.84 | ... | -
 | Fanout | 0.01 | 1 | 0.12 | ... | - | 1.15 | ... | -
Logic Gates | Inverter | 0.01 | 1 | 0.13 | ... | - | 1.19 | ... | -
 | Majority | 0.01 | 1 | 0.15 | ... | 0.15 | 1.41 | ... | 1.41
 | OR | 0.01 | 1 | 0.18 | ... | - | 1.30 | ... | -
 | NOR | 0.02 | 2 | 0.31 | ... | - | 2.49 | ... | -
 | ... | ... | ... | ... | ... | ... | ... | ... | ...

## Slide 11: Analysis Environment
Diagonal arrangement of clocking
Levelizing of netlist graph
Diagonal placement of each level
Routing
P&R Algorithm

## Slide 12: Analysis Environment
Synthesis:
  Synthesis library (*.lib) for QCA gate library
  Synopsys Design Compiler
  ABC (AIG, BDD)
EFPL Benchmarks
Flow
Benchmark name | Inputs | Outputs | AND nodes
Adder (adder) | 256 | 129 | 1020
Barrel shifter (barrel) | 135 | 128 | 3336
Max (max) | 512 | 130 | 2865
Sine (sin) | 24 | 25 | 5416
... | … | … | …

## Slide 13: Results
Area

## Slide 14: Results
Delay

## Slide 15: Results
Energy Dissipation

## Slide 16: Conclusions
QCA is a promising nanotechnology for low energy applications
Specific characteristics of QCA design require notable amount of interconnections
Here: Evaluation of this impact
Results indicate high impact of Interconnections with consequences on area, delay, energy
Requirements for future research:
  Comprehensive synthesis cost model for interconnections
  New synthesis strategies with emphasis on reduction of interconnections
  Exploration of new concepts (systolic arrays, logic duplication, …)

## Slide 17
Thank you!
frasillt@uni-bremen.de

## Slide 18: Evaluating the Impact of Interconnections in Quantum-dot Cellular Automata (QCA)
Frank Sill Torres1,2, Robert Wille1,3, Marcel Walter2, Philipp Niemann1,2, Daniel Große1,2, Rolf Drechsler1,2
1DFKI GmbH (Germany), 2University of Bremen (Germany)
3JKU Linz (Austria)