## Slide 1: Exploration of Technology Parameter Values of Integrated Circuits
Rodrigo Fonseca Rocha Soares – UFMG
Frank Sill Torres – DELT/UFMG
Dirk Timmermann – University of Rostock

## Slide 2
Focus / Principal idea:
Technology Parameter Exploration of Integrated Circuits
Standard-Cell Characterization Flow for Novel Technologies

## Slide 3: Outline
Motivation
Methodology
Results
Conclusion

## Slide 4: Motivation
Integrated circuit technologies offer two kind of parameters:
  Design parameters (e.g. transistor width, transistor length)
  Technology parameters (e.g. doping, oxide thickness)
Design parameters
  Constrained
  Modifiable by circuit designers
Technology parameters:
  Constrained
  Not accessible by circuit designers
  Can be oriented to consumer applications profiles (e.g. High performance / Low-power)
Technology Parameters

## Slide 5: Motivation
Question: How to chose values for technology parameters?
Several constraints: Ion vs. Ioff currents, area, gain, …
Interesting for:
  Technology engineers
  Researchers for novel technologies (CNTFET, SET, …)
Common approach:
  Analysis using selected cells (FO4 configuration)
  Sweep of input parameters (e.g. slope, input value, …)
Technology Parameter Values

## Slide 6: Motivation
Problem: Common solution not accurate enough
Example: Average CMOS PTM22 gains in relation to CMOS PTM32
Proposal:
  Analysis of technology parameter based on actual designs
Novel Approach
Chart: 
| PDP | tdelay | Pleak
PTM32
Actual Designs | 0.6 | 0.68 | 2.28
FO4 | 0.68 | 0.84 | 1.75
8%
16%
53%

## Slide 7: Methodology
Presentation
Principal ideas:
  Analysis of technology parameters impact using characterized standard cell library and test designs
  Interactive parametric exploration
Application of comercial tool(s) for standard cell library characterization
Technology can be given on Spice, Circuit, or Verilog-A level
Test designs oriented in future application of selected technology

## Slide 8: Methodology
Two step flow:
  Pre-Setup
  Technology Parameter Exploration
Pre-Setup
  Environment Setup
  Standard-cell representation
Technology parameter Exploration
  Standard-cell characterization
  Benchmark and analysis

## Slide 9: Methodology
Design of standard cell library with default parameter values
Extraction of parameters for look-up tables in characterization flow
Selection of most important technology parameters and its ranges for exploration
Pre-Setup Stage:

## Slide 10: Methodology
Start parameters with default values
Perform characterization and benchmark with actual designs
Figure of Merit evaluation and analysis
Iterate
Technology Parameter Exploration

## Slide 11: Results
Analyzed Technologies:
  PTM22 and PTM32 (based on Predictive Technology Model - PTM)
  FINFET10-HP FINFET10LL (based on PTM)
  CNTFET32 and CNTFET22 (based in Stanford CNFET Model)
Basic standard cell library (10 cells, different sizes, FlipFlop)
Test Designs:
  ISCAS suite: c1908, c2670, c3540, c5315, c7552
  ITC99 suite: b01, b05
Tools:
  Cell library characterization: SiliconSmart (Synopsys)
  Simulation: Virtuoso Analog Design Environment (Cadence)
Environment

## Slide 12: Results
Versus results for PTM32
Technology Comparison – Delay (tdelay)

## Slide 13: Results
Versus results for PTM32
Technology Comparison - Power Delay Product (PDP)

## Slide 14: Results
Versus results for PTM32
Technology Comparison – Leakage (Pleak)

## Slide 15: Results
Comparison of relation to PTM32 of FO4 analysis and proposed flow
Technology Comparison

## Slide 16: Results
Exemplary parameter exploration on CNTFET22 technology
Key parameter: tube diameter (high impact on ON/OFF current)
Note:
  Number of tubes (Ntubes): changes →
  Distance between tubes (pitch): constant
  Channel length (Lch): constant
Parameter Exploration

## Slide 17: Results
Results for delay in comparison to standard diameter (dCNT = 2nm)
Parameter Exploration

## Slide 18: Results
Results for dynamic power consumption (Pdyn) in comparison to standard diameter (dCNT = 2nm)
Parameter Exploration

## Slide 19: Results
Results for leakage in comparison to standard diameter
Parameter Exploration

## Slide 20: Results
Parameter Exploration
Figure of Merit with weights φ =1, γ = 1, γleak = 1.5
Chart: 
| 0 | 1 | 2 | 3
F | 32 | 103 | 20.6 | 28.4

## Slide 21: Conclusion
New flow for exploration of technologies parameters
Proposal of Figure of Merit for evaluation of technology parameter set
Approach based on actual designs
Increased the quality of predictions by up to 46%
Applied successfully in CNTFET based technology

## Slide 22
Thank you!
ART
OptMAlab / ART
www.asic-reliability.com

## Slide 23: EXTRA CNFET

## Slide 24: EXTRA FINFET

## Slide 25: EXTRA BULK
Gate
Drain
Source
Oxide
Substrate